## Slide 1: 19AIE112
INTRODUCTION TO ELECTRONICS

## Slide 2: GROUP-05
Divith Phogat [CB.EN.U4AIE20013]
Jayanth M[CB.EN.U4AIE20024]
Karnati Sai Prashanth[CB.EN.U4AIE20027]
Rachure Charith Sai [CB.EN.U4AIE20055]
Srikakolapu Venkata Sai Dhanush[CB.EN.U4AIE20068]

## Slide 3: PROJECT Design an RC phase shift oscillator circuit/circuits to generate a set of sinusoidal signals and combine them to generate a clock pulse of arbitrary frequency which drives a sequential digital up counter

## Slide 4: Presentation Overveiw 02 FF based counter Using the generated square wave as a clock to a FF based counter (counts up to 15) 04 working principle of RC phase shift oscillator and Output RC Phase shift Oscillator 01 Adder circuit Adding sinusoids with an adder circuit to generate a square wave 03
FINAL CIRCUIT

## Slide 5: Introduction

## Slide 6: OSCILLATOR An oscillator is a mechanical or electronic construction which produces oscillation depending on few variables. We all have devices which need oscillator, traditional clock that we all have in our home as a wall clock or wristwatch, various type of metal detectors, computers where microcontroller and microprocessors are involved all use oscillators, especially electronics oscillator which produces periodic signals. There are many types of Oscillators based on there configuration like Hartley Oscillator, Colpitts Oscillator, Wein Bridge Oscillator, Quartz Crystal Oscillator, Phase Shift Oscillator Circuit etc.

## Slide 8: RC Phase Shift Oscillator 01

## Slide 9
RC phase-shift oscillators use resistor-capacitor (RC) network (Figure 1) to provide the phase-shift required by the feedback signal. They have excellent frequency stability and can yield a pure sine wave for a wide range of loads.
Ideally a simple RC network is expected to have an output which leads the input by 90o.
However, in reality, the phase-difference will be less than this as the capacitor used in the circuit cannot be ideal. Mathematically the phase angle of the RC network is expressed as
Where, XC = 1/(2πfC) is the reactance of the capacitor C and R is the resistor.

## Slide 10
RC Phase Shift Oscillator using BJT
In this case, RC phase-shift oscillator is formed by cascading three RC phase-shift networks, each offering a phase-shift of 60o

## Slide 11
Working:
Here the collector resistor RC limits the collector current of the transistor, resistors R1 and R (nearest to the transistor) form the voltage divider network while the emitter resistor RE improves the stability. Next, the capacitors CE and Co are the emitter by-pass capacitor and the output DC decoupling capacitor, respectively. Further, the circuit also shows three RC networks employed in the feedback path.
This arrangement causes the output waveform to shift by 180o during its course of travel from output terminal to the base of the transistor. Next, this signal will be shifted again by 180o by the transistor in the circuit due to the fact that the phase-difference between the input and the output will be 180o in the case of common emitter configuration. This makes the net phase-difference to be 360o, satisfying the phase-difference condition. One more way of satisfying the phase-difference condition is to use four RC networks, each offering a phase-shift of 45o. Hence it can be concluded that the RC phase-shift oscillators can be designed in many ways as the number of RC networks in them is not fixed. However it is to be noted that, although an increase in the number of stages increases the frequency stability of the circuit, it also adversely affects the output frequency of the oscillator due to the loading effect.
Design an RC phase shift oscillator circuit/circuits to generate a set of sinusoidal signals and combine them to generate a clock pulse of arbitrary frequency which drives a sequential digital up counter

## Slide 12
The generalized expression for the frequency of oscillations produced by a RC phase-shift oscillator is given by
Where, N is the number of RC stages formed by the resistors R and the capacitors C.

## Slide 13
RC Phase Shift Oscillator using OP-Amp
RC phase-shift oscillator is a linear electronic oscillator circuit that produces a sine wave output.
It consists of an inverting amplifier element such as a transistor or op-amp with its output fed back to its input through a phase-shift network consisting of resistors and capacitors in a ladder network.
Each of the three RC networks in the feedback loop can provide a maximum phase shift approaching 90 degrees. Oscillation occurs at the frequency where the total phase shift through the three RC network is 180 degrees.
Inversion output at the output of op-amp itself produces the additional 180 degree to meet the requirement for oscillation of 360 degrees (or zero degree) phase shift around the feedback loop.

## Slide 14
Further, it is to be noted that the frequency of the RC phase-shift oscillators can be varied by changing either the resistors or the capacitors. However, in general, the resistors are kept constant while the capacitors are gang-tuned.
Applications
used as
(a). local oscillators for synchronous receivers
(b). musical instruments
(c). low and/or audio-frequency generators.

## Slide 15: Falstad Simulation:
OUTPUT
Click to add text
Link : RC Phase Shift Oscillator

## Slide 16
MATLAB Simulation :
Components Used :
Voltage sensor
Solver Configuration
Resistor
Ground
A/c Voltage Source
Op – AMP
Capacitor
Ps Simulink Converter

## Slide 17
Circuit Diagram :
OUTPUT:

## Slide 18: Adder circuit 02

## Slide 19
Summing amplifier using Op-amp
Summing amplifier is a type operational amplifier circuit which can be used to sum signals. The sum of the input signal is amplified by a certain factor and made available at the output .Any number of input signal can be summed using an op-amp. The circuit shown below is a three input summing amplifier in the inverting mode.

## Slide 20
In the circuit, the input signals Va,Vb,Vc are applied to the inverting input of the op-amp through input resistors Ra,Rb,Rc. Any number of input signals can be applied to the inverting input in the above manner. Rf is the feedback resistor. Non-inverting input of the op-amp is grounded using resistor Rm. RL is the load resistor. By applying kirchhoff’s current law at node V2 we get,
Ia+Ib+Ic = If+Ib
Since the input resistance of an ideal op-amp is close to infinity and has infinite gain. We can neglect Ib & V2. There for
Ia+Ib+Ic = If ……….(1)
Equation (1) can be rewritten as
(Va/Ra) + (Vb/Rb)+ (Vc/Rc) = (V2-Vo)/Rf
Neglecting V2,we get
Va/Ra + Vb/Rb + Vc/Rc = -Vo/Rf
Vo = -Rf ((Va/Ra)+(Vb/Rb)+(Vc/Rc))

## Slide 21
Vo = -((Rf/Ra )Va + (Rf/Rb) Vb + (Rf/Rc) Vc)……..(2)
If resistor Ra, Rb, Rc has same value ie; Ra=Rb=Rc=R, then equation (2) can be written as
Vo = -(Rf/R) x (Va + Vb +Vc)…………….(3)
If the values of Rf and R are made equal , then the equation becomes,
Vo = -(Va + Vb +Vc)

## Slide 22
Falstad Simulation:
OUTPUT:
Link: Summing Amplifier

## Slide 23: FF based counter 03

## Slide 24
What is a counter ?
A counter is a device which it can count any particular event on the basis of how many times that the particular event is occurred.
In digital circuits, the counter can count and store the number of time any particular event or process have occurred, depending on a clock signal.
Types of counter:
Asynchronous counter.
Synchronous counter.
For our project we will be using Synchronous counter, and in synchronous counter there are two types:
Synchronous up counter.
Synchronous down counter.
We will be using synchronous up counter for this project.

## Slide 25
4 bit Synchronous up counter
In Synchronous Counter, the external clock signal is connected to the clock input of every individual JK flip-flop within the counter so that all the flip-flops are clocked together simultaneously (in parallel) at the same time with results in no propagation delay.

## Slide 26
Link: 4 bit Synchronous up counter
Falstad Simulation:

## Slide 27: Final circuit 04

## Slide 28
We Generate a Square wave by adding odd harmonics of sinusoidal wave.
This produces a square of fundamental frequency.
Here we are taking first 5 odd harmonics of sine wave with fundamental frequency 50Hz.
On adding them it produces a 50 Hz square wave
Producing 50 Hz Square wave using Fourier Series

## Slide 29
Here we are taking first 2 odd harmonics of sine wave with fundamental frequency 150Hz.
On adding them it produces a 150 Hz square wave.
Producing a 150 Hz Square wave using Fourier Series

## Slide 30
Selecting R and C values of RC phase shift oscillator to generate a specific frequency.
For an RC phase shift oscillator, WKT the output frequency is
Here, we are using 3 RC stages(N=3).
Fixing the value of R as 1kΩ.
By selecting the required frequency, we can calculate the value of the Capacitor.
For 50Hz sine wave the value of capacitor required is 1.3μF.
Selecting appropriate values for each element.

## Slide 31
To get a square wave, we have to multiply the odd harmonics of the sine wave with its respective coefficients and add them.
Selected Feedback resistance, So the output is nearly 5V.
Resistance Values of Summing Amplifier.

## Slide 32
We are using Relays to produce multiple frequencies in a single circuit.
When the switch is in "OFF" state, we are generating 50HZ square wave.

## Slide 33
When the switch is in "ON" state, we are generating 150HZ square wave.

## Slide 34: Final circuit
Link : Final Circuit

## Slide 35: INGERENCE:
We have successfully built the RC phase shift oscillator and produced the various sinusoids. Then we connected RC phase shift oscillator with different frequencies and connected it to the summing amplifier.
Then, the total circuit including the summing amplifier is connected to the ff based counter and we observe results in Falstad circuit simulator.

## Slide 36: Conclusion:
We can conclude that we can also produce Square waves using Sine wave by using the concept Fourier series and with help of phase shift oscillator and summing amplifier.
Depending on the inputs of the summing amplifier (output of phase shift oscillator) the frequency of output waveform will be changing.
Which leads to change in the speed of the clock.

## Slide 37: Thank you